## Slide 1: DSP First, 2/e
Lecture 18
DFS: Discrete Fourier Series, and Windowing

## Slide 2: License Info for DSPFirst Slides
This work released under a Creative Commons License with the following terms:
Attribution
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees must give the original authors credit.
Non-Commercial
    The licensor permits others to copy, distribute, display, and perform the work. In return, licensees may not use the work for commercial purposes—unless they get the licensor's permission.
Share Alike
    The licensor permits others to distribute derivative works only under a license identical to the one that governs the licensor's work.
Full Text of the License
This (hidden) page should be kept with the presentation

## Slide 3: READING ASSIGNMENTS
This Lecture:
  Chapter 8, Sections 8-3, 8-5 & 8-6

## Slide 4: LECTURE OBJECTIVES
Discrete Fourier Series for periodic x[n]
  DFT of one period with scaling by 1/N gives scaled DFS coefficients
Windowing
  extract short sections from long signal

## Slide 5: Review
Discrete Fourier Transform (DFT)
DFT is frequency sampled DTFT
    For finite-length signals
DFT computation via FFT
  FFT of zero-padded signalmore freq samples
Transform pairs & properties (DTFT & DFT)

## Slide 6: Comparison: DFT and DTFT
Discrete Fourier Transform (DFT)
Inverse DFT
Discrete-time Fourier Transform (DTFT)
Inverse DTFT

## Slide 7: Inverse DFT always makes a periodic signal
Evaluate N-pt IDFT outside of [0,N-1]
Thus the IDFT synthesizes a periodic signal

## Slide 8: Fourier Series for Discrete-Time Signal
Given a periodic sequence x[n], how do we write it as a sum of sinusoids (or complex exponentials) ?
Which frequencies? How many? Fundamental ?
Exponentials must have the same period as x[n], which is N. There are only N possible exps.

## Slide 9: Discrete Fourier Series Representation (2)
Given the sequence x[n], how do we find ak?
Recall IDFT always synthesizes a periodic x[n]
So, we find ak by taking the
N-pt DFT of one period of x[n]
and then multiplying by 1/N

## Slide 10: Discrete Fourier Series (DFS)
Synthesis of a periodic signal x[n] = x[n+N]
Find ak by taking N-pt DFT
of one period of x[n]
and then multiplying by 1/N

## Slide 11: DFT of one period  DFS
Figure 8-12 Periodic sequence x[n] in (8.43) and the corresponding 40-point DFT spectrum X[k]. (a) Dark region indicates the 40-point interval (starting at n = 0) taken for analysis. (b) DFT magnitude spectrum. (c) DFT phase spectrum.
Can you get the DFS coeffs from this DFT ?

## Slide 12: DFS Synthesis Example
Recall negative frequencies in high indices for the DFT

## Slide 13: How is DFS related to cont-time Fourier Series ?
Fourier Series (from Chap. 3)
Need to obey the Nyquist rate: i.e., band-limited signal
Then sample

## Slide 14: How is DFS related to cont-time Fourier Series (2)
Band-limited Fourier Series (from Chap. 3)
Can be sampled to give periodic x[n]
Compare to DFS
Same coefficients

## Slide 15: Spectrum Analysis of a Periodic Signal x[n]

## Slide 16: Windows
Finite-Length signal (L) with positive values
  Extractor
  Truncator

## Slide 17: Von Hann Window (Time Domain)
Plot of Length-20 von Hann window

## Slide 18: Von Hann Window (Frequency Domain)
DTFT (magnitude) of Length-20 Hann window

## Slide 19: Window section of sinusoid, then DFT
Multiply the very long sinusoid by a window
  Take the N-pt DFT
    Finite number of frequencies (N)
  Finite signal length (L) = window length
Expectation: 2 narrow spectrum lines

## Slide 20: DTFT of Windowed Sinusoid (with different windows)
DTFT (magnitude) of windowed sinusoid
  Length-40 Hann window vs Length-40 Rectangular window
UnWeighted
Hann Window

## Slide 21: Change Window Length
DTFT (magnitude) of windowed sinusoid.
  Length-20 Hann window vs. Length-40 Hann window

## Slide 22: Challenge: find DFS for x[n] = sampled Dirichlet
Synthesis of a periodic signal, x[n] = x[n+N]
Find ak by taking N-pt DFT of one period of x[n] and then multiplying by 1/N